## Slide 1: Boulder City Municipal Airport Ground Vehicle Operator Training

## Slide 2: Purpose of this training
  …to educate & establish guidelines and assign responsibility for the safe operation of vehicles within the airport movement area (AMA)
  …to provide an overview of the handbook and provide you the necessary knowledge to drive in the AMA

## Slide 3: Why?
FAA States:
…responsibility rests with the airport operator to establish procedures and policies concerning vehicle access on airport.
…keep vehicular and pedestrian activity on the airside of the airport to a minimum…limited to those vehicles necessary to support the operation of aircraft services and maintenance of the airport.

## Slide 4: Outcome
After Viewing this presentation
Review for the Test
Pass the 20 question test regarding Procedures at BVU (questions from the presentation and the handbook)
You will get a badge indicating you are a “D”river and are authorized by airport management to drive in the Airport Movement Area AMA – Restricted from crossing or proceeding onto any Runways

## Slide 5: Topics covered
  Airport Terminology
  Airport Layout
  Vehicle Operations
  Situational Awareness
  Airport Markings and Signage
  Radio Communications
  Review Airport HOT SPOTS
  Airport Safety

## Slide 6: Terminology
Concepts and terminology you should be familiar with…

## Slide 7: Airside
…within the fence
taxiways, runways, ramps, perimeter road, taxilanes, buildings, safety areas

## Slide 8: Hot Spot
A location on an Airport Movement Area with a history of potential risk of collision or runway incursion, and where heightened attention by pilots and drivers is necessary.

## Slide 9: Airport Movement Area
areas used for takeoff, landing, taxing, and hovering of aircraft
Taxiway Delta holding short Runway 15

## Slide 10: Airport Movement Areas

## Slide 11: Ramp Area
…accommodate aircraft for the purposes of parking, loading and unloading of passengers or cargo, refueling, or maintenance.
All companies on the airport each have their own ramp areas, and some may operate from the City’s Transient Ramp.

## Slide 12: Airport Basics
Runways
Taxiways

## Slide 13: Runway Layout
33
15
9
27
x
x

## Slide 14: Runways - defined
Purpose to allow aircraft to take-off and land

## Slide 15: Runways - Markings
All pavement markings are White
Runway Designator
Threshold
Edge
Centerline
9

## Slide 16: Runways - lighting
White runway edge lights are white

## Slide 17: Runways – lighting
Runway threshold lights
  Two-sided: Red/Green
  Runway End/Beginning

## Slide 18: Runway Signs
Hold Short Signs
  Red Background/White Lettering
Hold Short pavement markings
  Double Solid Line – you cannot cross without an escort.

## Slide 19: Taxiways - defined
A path on an airport connecting runways with ramps, hangars, terminals and other facilities.

## Slide 20: Taxiway Layout
A
D
D
B
B

## Slide 21: Taxiway - markings
Yellow
Taxiway Centerline
Runway Hold Short Markings

## Slide 22: Taxiway - lighting
Blue taxiway edge light or reflectors

## Slide 23: Taxiway - signage
A = Alpha
D = Delta
D = Delta
B = Bravo
Taxiways are phonetically pronounced as listed below, a full list of can be found in the Ground Vehicle Operations Manual.

## Slide 24: Taxiway - signage
Location Sign has a black background and yellow lettering
Directional…which taxiway you’re approaching and their direction.
Good way to remember is Black is where your at and yellow is where to go

## Slide 25: Taxiway - signage
Taxiway & Hold Short Sign – indicated you are approaching a runway and must stop at the sign and get an escort before proceeding out on the runway.

## Slide 26: Hot Spot - Taxiway Delta
Taxiway Delta between Taxiway Alpha and Bravo is designated and airport Hot Spot:
    A location with a history of potential risk of collision and where heightened attention by pilots and drivers is necessary.

## Slide 27: HOT SPOT
Helicopters cross Taxiway Delta very low to/from the FATOs or Heli Spot 1,2,3, 4
(Final Approach & Take-off Area)
USE EXTREME CAUTION
When traveling on Taxiway Delta
Stop

## Slide 28: Situational Awareness
…is a perception of environmental elements with respect to time and space…it is how you understand information, event’s and how one’s actions will impact events– both immediately and in the future.
…maintain positive situational awareness when on the airfield – EVERYWHERE you go

## Slide 29: Situational Awareness Paramount to your Personal Safety

## Slide 30: Situational Awareness Paramount to your Personal Safety

## Slide 31: Who Can Drive in the AMA?
To Operate in the AMA you must:
    Authorization by your supervisor AND
    Approved by the Airport Management Office
Runway Access is Not Permitted
    Escort by Airport Management Only to proceed on Runways

## Slide 32: Vehicles in AMA
NO Privately Owned Vehicles
Authorized Vehicles ONLY
    Authorized by Airport Management ONLY
    Authorized Vehicles will have a permit sticker on the rear bumper
BVU
AMA
066

## Slide 33: Access Gates
Vehicle Gate #68
Pedestrian Gate #4
Pedestrian Gate #16
Vehicle Gate #8
Vehicle Gate #1
Gates are located around the airport and access to these gates are limited by the company you work for and the locations you operate from.
This will be reviewed at the time you receive your badge

## Slide 34: Airport Speed Limit
Airport Airside Speed Limit 10mph

## Slide 35: Vehicles
Commercial Vehicle
  …any vehicle on airside used for the support of aircraft.

## Slide 36: Vehicles
Privately Owned…any vehicle on airside used for purpose other than commercial or emergency
Permitted in the Hangar and North Tie Down Only
Example –pilot driving on the taxi-lane to access his or her aircraft.

## Slide 37: Vehicles
Emergency Vehicles…operated by local agencies to respond to an emergency situation.
Give way to emergency response vehicles.

## Slide 38: Driving on the Airport
Ensure your Beacon and Radio are turned ON
Stop-Look-Listen for Aircraft
    Small aircraft can blend in with the surroundings
    Helicopters transition from many different locations
Monitor the Aircraft Radio for aircraft movements on UNICOM/CTAF 122.7
Aircraft Always have Right of Way

## Slide 39: Unicom-CTAF Purpose Frequency 122.7 – Monitor at ALL TIMES
For collision avoidance
Communicate if you must, but keep it to a minimum as the radio is congested with aircraft announcing position reports
Speaking over the UNICOM/ CTAF
  Listen for space to talk
  Know exactly what you want to say before you say it…rehearse it in your head.
  Be as concise as possible

## Slide 40: Airfield Accidents
Accident – a collision between one aircraft or vehicle and another aircraft, vehicle, person, or object which results in property damage personal injury, or death.
Accidents are caused by:
  human error,
  unfamiliar with an airport, or
  loss of situational awareness.

## Slide 41: Vehicle Accidents
Vehicle Accident - If a vehicle accident occurs STOP and:
  Remain at the scene of the accident
  Immediately notify 911 and Airport Management.
  If capable and it is safe to do so, assist those who are injured
  Provide information to Airport Management or Police

## Slide 42: Aircraft Accident
Aircraft Accident can be an aircraft that crashed or has a flat tire, overrun, fire, etc, stalled.
Who to notify:
  911
  Airport Management – 702-293-9405
  FBO – Boulder City Aviation Services - 702-638-3205
Aircraft must not be moved without prior permission from Airport Management.
Notes: If

## Slide 43: Airfield Accidents
Review
  Call 911
  No Matter the size it must be reported to Airport Management
  Never move an aircraft until you have authorization from Airport Management
  Stay and provide a statement to Police/Airport Management

## Slide 44: Escorting Procedures
Provided to:
    Vendors, Inventory/Supply Delivery, Contractor, Mechanic
Your Responsibilities:
    Notify individual they are operating in the AMA
    Make sure individual remains under your control
You are ultimately responsible for the person you are escorting!

## Slide 45: Security
When operating on the Airport:
Airport Access Badge/Airport ID Visible
When you enter/leave the airport , watch the gate shut – completely.
Gates – broken or malfunctioning report
    Dispatch 702-293-9224 after hours
    Airport Staff 702-293-9405 7am-5pm

## Slide 47: Violations
What is a violation?
  Any observed or report of a person not following the rules set forth in the airports ground vehicle program.
  Carless and reckless behavior on the airfield.
Penalties for violating a rule is:
  Removal of driving privileges
  Retraining
  Fine of not more than $1000 (day 9-4-6 of the Boulder City Code )

## Slide 48: Violations
Violation Process
    Written Warning
    1st Notice – Retraining within 30 days & $25 fee
    2nd Notice – Suspended privileges for 30 days $ 25 fee
    3rd Notice – Possible revocation of privileges
Airport Management reserves the right to immediately revoke the driving privileges of violators who cause an accident, incident or is careless/reckless on the airport.

## Slide 49: Foreign Object Debris
FOD – is a substance, debris, or article which could potentially cause damage to an aircraft.
Common Types of FOD found at BVU:
  Screws
  Rocks, sand, dirt
  Small tools
  Trash; paper, cups, bottles, cans, cardboard, plastic bags, fast food wrappers, food, fruit peels, cigarette butts, etc.

## Slide 50: FOD . . . Not Your Problem ? Think Again!!
Did you Know:
Misplaced tools and parts are the most common form of FOD. They cause damage, lost time, and lost productivity.
Items such as papers, bottles, cans, loose coins, plastic bags, personal devices, pencils, and pens can cause serious FOD damages

## Slide 51: Foreign Object Debris
Potential hazard to all aircraft owners and tenants and passengers.
Creating:
  Flight delays
  Aircraft damage
  Accident/Incident
  Injury to ramp personnel

## Slide 52: Foreign Object Debris
What does it look like?

## Slide 53: Foreign Object Debris
Littering Food Items can become a wildlife attractant.
Wildlife present on the airfield pose as another risk to aircraft: Wildlife Strike

## Slide 54: Clean-As-You-Go
What does this mean?
  During your normal daily routine pickup the out of place and unordinary items you find along the way.
    Anything you see airside or landside – If you see garbage spilling out of the dumpster on a windy day this can become FOD across the airport.
    Don’t think the next guy will get it…Take responsibility and help keep our airport FOD FREE.

## Slide 55: Remember
Airport Access is a Privilege – Not a right.
Not for personal use.

## Slide 56: Be sure to have reviewed the Ground Vehicle Operations Manual along with watching this presentation. Visit www.flybvu.com for a copy of the manual. Review the airfield layout as you will be asked questions regarding this on the test!! The test questions will be drawn from both resources. Visit the Airport Admiration Office for testing.
Review & Testing